## Slide 1: EN.601.414/614 Computer Networks Final Review
Xin Jin
Fall 2020 (TuTh 1:30-2:45pm on Zoom)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Final Exam
Time: 7pm-9pm, Wednesday, December 16
Location: online
Form: open-book
  Can use slides for reference
  Can use a calculator
  Anything else is prohibited
Focus on materials after midterm
  Materials before midterm will be tested, but not a focus
Senior option
  Your final exam score will be the same as your midterm score
Contact the course staff on piazza before December 11 (this Friday) if you want to use the senior option or if you need any special accommodation

## Slide 3: This review
Walk through what you’re expected to know at this point: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 4: The networking stack
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 5: Topics
Network layer (lectures 12–15)
  Intra-domain routing
  Inter-domain routing
Link layer (lectures 17–18)
  Ethernet
Topics in networking (lectures 16, 19–21)
  Programmable networks
  Wireless
  Security
  Misc

## Slide 6: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 7: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 8: Routing: Local vs. global view
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take

## Slide 9: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Notes: What could go wrong?

## Slide 10: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 11: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 12: Intra-domain routing
Link-state (LS) routing protocol
  Dijkstra’s algorithm
  Broadcast neighbors’ info to everyone
Distance vector (DV) routing protocol
  Bellman-Ford algorithm
  Gossip to neighbors about everyone

## Slide 13: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 14: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (error propagates)

## Slide 15: Addressing is key to scalable inter-domain routing
Ability to aggregate addresses is crucial for
  State: Small forwarding tables at routers
    Much less than the number of hosts
  Churn: Limited rate of change in routing tables

## Slide 16: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 17: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 18: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 19: Topology & policy shaped by inter-AS business relationship
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic

## Slide 20: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 21: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 22: Valley-Free Routing
Number links as (+1, 0, -1) for customer-to-provider, peer and provider-to-customer
In any path should only see sequence of +1, followed by at most one 0, followed by sequence of -1
Example question: show why the traffic is allowed or not allowed in the previous slide with valley-free routing

## Slide 23: Example Question
Show why the traffic is allowed or not allowed with valley-free routing
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed

## Slide 24: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 25: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 26: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability
  E.g., OSPF, RIP

## Slide 27: eBGP, iBGP, and IGP together
Learn routes to external destination using eBGP
Distribute externally learned routes internally using iBGP
Travel shortest path to egress using IGP

## Slide 28: Topics
Network layer (lectures 12–15)
  Intra-domain routing
  Inter-domain routing
Link layer (lectures 17–18)
  Ethernet
Topics in networking (lectures 16, 19–21)
  Programmable networks
  Wireless
  Security
  Misc

## Slide 29: Data link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection and correction

## Slide 30: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 31: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 32: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does not eliminate all collisions
  Why?

## Slide 33: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 34: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 35: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 36: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability

## Slide 37: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 38: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 39: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 40: Example Question
Describe the process for 1.2.3.48 to access www.foo.com hosted on 5.6.7.10
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 41: Topics
Network layer (lectures 12–15)
  Intra-domain routing
  Inter-domain routing
Link layer (lectures 17–18)
  Ethernet
Topics in networking (lectures 16, 19–21)
  Programmable networks
  Wireless
  Security
  Misc

## Slide 42: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
PISA
Networking
P4
Compiler
>>>

## Slide 43: PISA: Protocol Independent Switch Architecture
Match+Action
Memory
ALU
Programmable
Parser
Programmer declares which
headers are recognized
Programmer declares what
tables are needed and how packets are processed
All stages are identical – makes PISA a good “compiler target”
Notes: PISA chips are also built around a pipeline. But in PISA, all the pipeline stages are all IDENTICAL. They initially don’t know anything about protocols – they are sitting waiting to receive instructions from the compiler.
The basic operations of each stage is called “Match + Action” – In each stage, there is a set of memories which match on headers,
Depending on the match, an action is applied to the header by an ALU. And then the header is passed to the next stage, and so on.
A PISA chip is initially blank – it doesn’t know about any protocols.
The P4 programmer tells the programmable parser what packet headers it should recognize.
If a new header is developed, we add it to the set of headers the parser recognizes.
Let’s take a closer look at how a packet is processed …..

## Slide 44: Summary of Programamable Networks
Chip speed: We can now make programmable switch chips as fast as fixed ones.
Chip technology: The difference in chip area and power between “programmable” and “fixed function” is going away.
Chip complexity: There are now too many protocols to correctly hard-code in silicon.
New ideas: Beautiful new ideas are owned by the programmer, not the chip designer.
Level playing field: Lets us create a solid platform, an abstraction layer, upon which more will be built
To learn more, visit P4.org
Notes: Chip technology: The difference in chip area and power between “programmable” and “fixed function” is going away.
Chip complexity: There are now too many protocols to correctly hard-code in silicon.
Chip architecture: Instruction set is now known.
Chip speed: We can now make programmable switch chips as fast as fixed ones.
New ideas: Beautiful new ideas are owned by the programmer, not the chip designer.
More reliable network: Greater visibility means failures diagnosed faster. Fixes deployed quickly.

## Slide 45: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving at destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 46: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues
  Hidden terminal problem

## Slide 47: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 48: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Notes: 48

## Slide 49: General goals for communication security: CIA
Confidentiality
  No one read our communication
  Cryptography
Message Integrity
  No one can modify our communication w/o detection
  Verification
Availability and Authentication
  Redundancy, DoS/DDoS prevention
  Only we can access our data and communicate on our behalf

## Slide 50: Computer networks is a fast growing area
Software-Defined Networking
Cloud Computing
Network Virtualization
Network Testing and Verification
Big Network Data Processing
AI and Networking
Internet of Things
Bitcoin and Blockchain

## Slide 51: Summary
Final exam:
  Time: 7pm-9pm, Wednesday, December 16
  Location: online
2021 Spring: EN.601.714 Advanced Computer Networks
THANK YOU SO MUCH!!!

## Slide 52: Thanks! Q&A